## Slide 1: UU-PCBA-MANT
Dual-band BRS/CBRS path antenna for Massive MIMO
Pre-production Release
2020-01-07

## Slide 2: Front view of panel & Perspective view of MCX connector with vias
Center pin and bottom : PTH ; top 2 : NPTH

## Slide 3: Back view of panel

## Slide 4: Side view
Need to stack 2 boards for bottom layer substrate. (Max thickness of RO3003 : 1.52mm??)

## Slide 5: S11
CBRS: good specs
2.5 GHz: Center at ~ 2.54GHz and dips only to -14 dB (but radiation efficiency is as desired, shown in next slide)

## Slide 6: Total (radiation) efficiency
2.5G: -2dB BW of 150 MHz (63% efficiency). Peak efficiency : -0.8 dB (83% efficiency)
CBRS: -2dB BW of 200 MHz (63% efficiency). Peak efficiency : -0.44 dB (90% efficiency)

## Slide 7: Farfield gain patterns (2.5 GHz band)
Gain : 2.99 @ 2.45GHz ; 3.5 @ 2.5GHz ; 3 @ 2.57GHz
HP Beam width : varies between 80-90 degrees

## Slide 8: Farfield gain patterns (CBRS)
Gain : 3.4 @ 3.55GHz ; 4.1 @ 3.63GHz ; 3.2 @ 3.7GHz
HP Beam width : varies between 80-90 degrees

## Slide 9: Sensitivity of total efficiency due to R (radius of patch)
R = 15.4mm (shown in black) : Exact value
Perturbation by +/- 0.05mm leads to negligible variation in performance
Total efficiency is shown in absolute units here.

## Slide 10: Sensitivity of total efficiency due to r1 and r2 (radius of inner and outer arc slots
r1 = 14.6mm & r2 = 13mm(shown in black) : Exact value
Perturbation of r1 by +/- 0.05mm leads to ~20MHz shift on either side (both bands)
Similar perturbation leads to ~ 15 MHz on either side only in the 2.5GHz band

## Slide 11: Sensitivity of total efficiency due to Rogers Dk
Dk = 3 (shown in black) : Exact value
Perturbation by +/- 0.05 leads to freq shift of 20 MHz on either side (both bands)
Sensitivity due to perturbations in all other parameters (geometry of feedlines, stubs, etc.) is minimal as well.